## Slide 1: IEEE 754 Standard Floating-point multiplication using Weighted 2-stage Booth algorithm and Carry Look-ahead Adder
Lê Thanh Hải 1851027
Phạm Tấn Khải 1851081
Instructor: Ph.D. Trần Hoàng Linh
Capstone I

## Slide 2: Contents
Introduction
1
Theory
2
Design and Implementation
3
Conclusion
4

## Slide 3: Introduction
Reasons and target of this project?
  IEEE 754 Standard floating-point is the most common representation today for real numbers on computers.
  A multiplier is one of the hardware blocks which generally occupies a significant chip area and is required to be minimized. A lot of applications in which multiplier blocks role an important unit, such as digital signal processing systems or computational techniques.
  The main objective is to increase the speed of execution by implementing certain algorithms for multiplying two floating-point numbers.

## Slide 4: IEEE 754 STANDARD (32 bits)
Sign: 0 for positive; 1 for negative
Exponent: from 1 to 254
special case: x 000…000 is ruled as ±0 (+ or – depends on x).
Sign (a bit) | Exponent (8 bits) | Mantissa (23 bits)
6.25 = 110.01 = 1.1001 22 
0 10000001 10010000000000000000000

## Slide 5: Floating-point multiplication
+
-
Check overflow/underflow
Normalizer
Multiplier
Final result (32 bits)
S1 S2 E1 E2 M1 M2
127

## Slide 6: Booth algorithm
Booth’s multiplication is an algorithm for multiplying two’s complement representation of signed binary numbers [1]. The algorithm is named to the credit of Andrew Donald Booth, who proposed it in 1950 [2].
In order to multiply two’s complement binary numbers, X*Y, Booth's algorithm implicitly appends a bit y-1 = 0 on the right of Y’s LSB. It examines the pair of bits yi and yi-1 by executing the iterations starting from i = 0 to i = N-1. Following execution takes place on comparison:
The product in accumulator P is left unchanged if the compared bits are equal.
The multiplicand times 2i is added to P when yi = 0 and yi-1 = 1
The multiplicand times 2i is subtracted from P when yi = 1 and yi-1 = 0.
Bit |  | Operation
20 | 2-1 | 
Yi | Yi-1 | 
0 | 0 | 0
0 | 1 | +X
1 | 0 | -X
1 | 1 | 0
Original Booth encoder [3]

## Slide 7: Modified Booth algorithm
Improve parallelism due to grouping three bits consecutive concurrently
Reduce the number of PPs up to 2 times in comparison with conventional multiplication.
Y7 Y6 Y5 Y4 Y3 Y2 Y1 Y0 Y-1
Yi+1 | Yi | Yi-1 | Operation | Meaning
0 | 0 | 0 | 0 | 
0 | 0 | 1 | +X | 
0 | 1 | 0 | +X | 
0 | 1 | 1 | +2*X | Shift left X
1 | 0 | 0 | -2*X | 
1 | 0 | 1 | -X | 2’complement of X
1 | 1 | 0 | -X | 
1 | 1 | 1 | 0 | 

## Slide 8: Modified Booth algorithm
The number of PPs can still be reduced using higher radix Booth encoder such as 8-radix, 16-radix or 32-radix encoder.
There are two main problems related to higher radix encoder’s drawbacks. First, extra adder logics are required for higher radix, not just shift bits as in radix-4. Second, larger input MUX are required in the higher radix multiplier.
HOWEVER !!!
Number | BOOTH ENCODER | NO. OF CELLS | TOTAL AREA
1 | Radix 2 | 9426 | 27569
2 | Radix 4 | 1690 | 3959
3 | Radix 8 | 2280 | 4359
4 | Radix 16 | 14672 | 32973
5 | Radix 32 | 25703 | 57091
Number | BOOTH ENCODER | TIME DELAY (ns)
1 | Radix 2 | 23.382
2 | Radix 4 | 13.993
3 | Radix 8 | 14.810
4 | Radix 16 | 26.581
5 | Radix 32 | 27.729
Comparison between different radix Booth algorithm [4]

## Slide 9: Radix-16 booth multiplier using weighted 2-stage Booth algorithm
PP
PP
Bit |  | Operation
20 | 2-1 | 
Yi | Yi-1 | 
0 | 0 | 0
0 | 1 | +X
1 | 0 | -X
1 | 1 | 0

## Slide 10: Radix-16 booth multiplier using weighted 2-stage Booth algorithm
PP
PP
0
X
2X
+
4X
+
+
+
8X
00000 | 0
00001; 00010 | +1*X
00011; 00100 | +2*X
00101; 00110 | +3*X
00111; 01000 | +4*X
01001; 01010 | +5*X
01011; 01100 | +6*X
01101; 01110 | +7*X
01111 | +8*X
11111 | 0
11110; 11101 | -1*X
11100; 11011 | -2*X
11010; 11001 | -3*X
11000; 10111 | -4*X
10110; 10101 | -5*X
10100; 10011 | -6*X
10010; 10001 | -7*X
10000 | -8*X

## Slide 11: Radix-16 booth multiplier using weighted 2-stage Booth algorithm
Yg+3 Yg+2 Yg+1 Yg Yg-1 | PP | Yg+1 Yg Yg-1 | Base PP | Yg+3 Yg+2 Yg+1 | Weighted PP | 2-stage PP (Base PP + Weighted PP)
00000 | 0 | 000 | 0F | 000 | 0F | 0F
00001 | +1 * X | 001 | 1F |  |  | 1F
00010 | +1 * X | 010 | 1F |  |  | 1F
00011 | +2 * X | 011 | 2F |  |  | 2F
00100 | +2 * X | 100 | -2F | 001 | 4F | 2F
00101 | +3 * X | 101 | -1F |  |  | 3F
00110 | +3 * X | 110 | -1F |  |  | 3F
00111 | +4 * X | 111 | 0F |  |  | 4F
01000 | +4 * X | 000 | 0F | 010 | 4F | 4F
01001 | +5 * X | 001 | 1F |  |  | 5F
01010 | +5 * X | 010 | 1F |  |  | 5F
01011 | +6 * X | 011 | 2F |  |  | 6F
01100 | +6 * X | 100 | -2F | 011 | 8F | 6F
01101 | +7 * X | 101 | -1F |  |  | 7F
01110 | +7 * X | 110 | -1F |  |  | 7F
01111 | +8 * X | 111 | 0F |  |  | 8F
10000 | -8 * X | 000 | 0F | 100 | -8F | -8F
10001 | -7 * X | 001 | 1F |  |  | -7F
10010 | -7 * X | 010 | 1F |  |  | -7F
10011 | -6 * X | 011 | 2F |  |  | -6F
10100 | -6 * X | 100 | -2F | 101 | -4F | -6F
10101 | -5 * X | 101 | -1F |  |  | -5F
10110 | -5 * X | 110 | -1F |  |  | -5F
10111 | -4 * X | 111 | 0F |  |  | -4F
11000 | -4 * X | 000 | 0F | 110 | -4F | -4F
11001 | -3 * X | 001 | 1F |  |  | -3F
11010 | -3 * X | 010 | 1F |  |  | -3F
11011 | -2 * X | 011 | 2F |  |  | -2F
11100 | -2 * X | 100 | -2F | 111 | 0F | -2F
11101 | -1 * X | 101 | -1F |  |  | -F
11110 | -1 * X | 110 | -1F |  |  | -F
11111 | 0 | 111 | 0F |  |  | 0F
Yi+1 Yi Yi-1
Yi+3 Yi+2 Yi+1
5-1 MUX
5-1 MUX
0
X
-X
2X
-2X
0
4X
-4X
8X
-8X
Modified (Radix-4) Booth algorithm
Base PP
Weight PP
Schematic of weighted 2-stage Booth encoder for radix 16 [5]

## Slide 12
Ripple Carry Adder
Full Adder
Full Adder
Full Adder
Full Adder
A3 B3 A2 B2 A1 B1 A0 B0
S3 S2 S1 S0
C4 C3 C2 C1 C0
Ripple Carry Adder (RCA)
Each FA block must wait for the carry to arrive from its previous block. Hence, there will be a considerable time delay (carry propagation delay).
 Calculating with a number has larger bits, it becomes less efficient regardless its simplicity.

## Slide 13
Carry Look-ahead Adder
A | B | Cin | Cout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
(A xor B) and Cin
A and B
Full Adder truth table

## Slide 14
Carry Look-ahead Adder
A xor B  called “carry generate” or G
A and B  called “carry propagate” or P
Cout = G + P . Cin
 Expanding with any FA blocks, the general equation becomes Cn = Gn + Pn . Cn-1
C1 = G1 + P1 . C0
C2 = G2 + P2 . (G1 + P1 . C0) = G2 + P2 . G1 + P2 . P1 . C0
C3 = G3 + P3 . (G2 + P2 . G1 + P2 . P1 . C0) = G3 + P3 . G2 + P3 . P2 . G1 + P3 . P2 . P1 . C0
etc.
Any element is available (as they depend only on inputs, that are A, B, C0)
The delay time now is the same for any carry bitfaster add operations are provided. However, CLA is complicated as the number of variables increase.

## Slide 15: DESIGN AND IMPLEMENTATION
Floating Point Multiplier
First FP number (X)
Second FP number (Y)
Exponent (8 bits)
Sign (1 bit)
Underflow (1 bit)
Overflow (1 bit)
Mantissa (23 bits)

## Slide 16: DESIGN AND IMPLEMENTATION
Exponent calculator
XOR
Mantissa Multiplier
NORMALIZATION-UNIT
Overflow/underflow?
M1
M2
E1
E2
S1
S2

## Slide 17: DESIGN AND IMPLEMENTATION
Pre-process of exponent calculator
  Special cases
  F
E:11111111
overflow
E:00000000
underflow
exponent calculator
T
T
F

## Slide 18: DESIGN AND IMPLEMENTATION
Exponent calculator
  This sub-block adds the exponents of two FP numbers and then minus the bias (12710) to get the exponent before normalizing. Before calculating, they are extended to 9 bits by adding bit 0 to the left of MSB.
  The bit just added plays a role as an announcement of overflow/underflow.
9-bit RCA
9-bit RCA
E1
E2
127

## Slide 19: DESIGN AND IMPLEMENTATION
Mantissa multiplier
  Pre-process
  Bit 0 must be added to the right of LSB of the multiplier Y before calculating.
  Booth algorithm is used for signed multiplication, and in this situation, the “hidden bit” 1 accidentally indicates the negative number. This is wrong because mantissa multiplication is an unsigned one. Extending multiplier and multiplicand by adding “virtual” bit 0, which informs that they are an unsigned number.
  00001                       0
0
0000
0000
Multiplicand: 28 bits
Multiplier: 29 bits

## Slide 20: DESIGN AND IMPLEMENTATION
Mantissa multiplier
Multiplicand (28 bits)
Weighted PP encoder
0
4*X
8*X
-4*X
-8*X
Base PP encoder
0
X
2*X
-X
-2*X
    
31 bits

## Slide 21: DESIGN AND IMPLEMENTATION
Mantissa multiplier
Weighted 2-stage Booth algorithm block
LSB    Multiplier (29 bits)    MSB
CLAs
5 bits
X
<< 4 bits
<< 8 bits
<< 12 bits
<< 16 bits
<< 20 bits
<< 24 bits

## Slide 22: DESIGN AND IMPLEMENTATION

## Slide 23: DESIGN AND IMPLEMENTATION
Underflow
Overflow
0 0xxx xxxx ?
1 xxxx xxxx ?
1111 1111 or 0000 0000 ?
No overflow/underflow
9-bit RCA
9-bit RCA
Ex Ey
127
T
T
F
F: after normalization
T: all 0s
T: all 1s
F

## Slide 24: RESULT
x | -79.85546875 | -45,625 | -521.52301025390625 | -1.31831126611e+35
y | 786 | -654321.5 | 0 | 1.44932046111e+13
Calculated result | -62766.3984375 | 29853418 | -0 | NA
Exact result | -62766.3984375 | 29853418.4375 | 0 | NA
Overflow | 0 | 0 | 0 | 1
Underflow | 0 | 0 | 1 | 0

## Slide 25: CONCLUSIONS
Cannot multiply all real numbers in decimal as they cannot represent in IEEE-754 exactly.
The input and output are represented in binary, which is not as friendly as decimal representation.
Single FP (32 bits), in some cases, do not have enough bits to ensure the accuracy.
Another method to multiply 2 numbers represented in IEEE-754, which also improves the speed,
Inform the overflow/underflow of the calculation.
Applying successfully some algorithms of signed multiplication into our FP multiplication design.

## Slide 26: DEVELOPMENTS
The design can be upgraded to double FP IEEE-754 (64 bits), which gives us a more exact representation of the FP number.
Build a converter from decimal to IEEE 754 standard representation and vice versa. This converter allows users to input decimal numbers, which are familiar to us.

## Slide 27: REFERENCES
[1] Ila Chaudhary, Romika Choudhary, Gagandeep Kaur, Ashish Vats and Deepika Kularia, “Design and Comparison of High-speed Radix-8 and Radix-16 Booth’s Multipliers”, International Journal of Computer Applications (0975 – 8887), Volume 181 – No.2, July 2018.
[2] Andrew D. Booth, “A signed binary multiplication technique”,1950.
[3] Mervat Mohammed Adel Mahmoud, “A parallel binary/decimal fixed-point multiplier with binary partial products accumulation”, faculty of Engineering, Cairo university, 2011.
[4] JasbirKaur, Sumit Kumar, “PERFORMANCE COMPARISON OF HIGHER RADIX BOOTH MULTIPLIER USING 45nm TECHNOLOGY,” IJIRSET (An ISO 3297: 2007 Certified Organization), Vol. 5, Issue 1, January 2016, ISSN(Online): 2319-8753, ISSN (Print): 2347-6710.
[5] Hyunpil Kim, Sangook, “Radix 16 booth multiplier using novel weighted 2-stage booth algorithm” IEICE Electronics express, vol. 11, no. 13, June 2014.
[6] V Rajaraman, “IEEE Standard for Floating Point Numbers”, January 2016.
[7] Naresh Grover, M.K.Soni, “Design of FPGA based 32-bit Floating Point Arithmetic Unit and verification of its VHDL code using MATLAB”, Published Online February 2014 in MECS (available at http://www.mecs-press.org/) DOI: 10.5815/ijieeb.2014.01.01.
[8] O. L. MacSorley, “High-speed arithmetic in binary computers”, Proc. IRE, Jan. 1961, vol. 49, pp. 67-91.

## Slide 28
THANK YOU !!!